ELECTRICITY 1

- Copy and complete the table for the electrical devices shown

| Component | Symbol | Main Energy change |
| --- | --- | --- |
|  |  | Electrical to sound |
| Solar cell |  |  |
|  |  | Heat to electrical |
| Microphone |  |  |

(6)

- Where does the energy change take place in a filament lamp		(1)

- Where does the energy change take place in a fluorescent tube		(1)

- The fluorescent tube is said to be more efficient than the filament lamp. Copy and complete the following sentence. “ This means that for the same ____________ energy input the fluorescent tube produces more ___________ energy than the filament lamp. In a filament lamp more of the input energy is changed to _________ energy than in the fluorescent tube.			(3)

- The diagram below shows the input and output energies to and from a power station

  - How does the input energy compare with output energy

Give a reason for this.							(2)

ELECTRICITY 2

- What are the two types of electrical charge					(2)

- Copy and complete. Like charges _____________ Unlike charges ______ (2)

3.   What is meant by

(a) Alternating current

(b) Direct current							(2)

4.   	(a)	What is the value of the mains voltage in Scotland?		(1)

(b)	What is the frequency of the mains supply? 			(1)

5.	Construct a table showing the following components with their correct symbol:

Cell, bulb, resistor, diode, fuse, ammeter                                                       (3)

6.	Look at this oscilloscope pattern:

(a)	Is this trace representing ac or dc input?                                            (1)

(b)If the gain is set at 2 V per division, what is

the peak voltage of the trace?                       (1)

7. How does the peak value of an alternating voltage compare to its quoted value?										(1)

8.      (a) Calculate the charge that passes along a wire if a current of 10 A flows for 30 seconds.									(2)

(b) Calculate the charge that passes through a bulb if it draws a current of 500 mA for 8 seconds.								(2)

(c) 12 Coulombs pass through a lamp in 6 seconds. What is the current     	flowing through the lamp?	                                                                        (2)

ELECTRICITY 3

1. An electron is projected into an electric field between two parallel plates as shown

(a) Copy and complete the diagram to show the path of the electron through 	the field

(b)Copy and complete the diagram if a proton was used instead of an electron

(2)

2. Copy and complete the sentences below using the following words to fill in the gaps.

Current		Charge		Voltage

(a) ________________ is the rate of flow of _________________

(b)  A measure of the energy given to the charge carrier is called the ________     	of the supply									(3)

3. Draw this circuit diagram carefully in your homework jotter, adding the circuit symbol for an ammeter to measure the current through lamp L. Then add the circuit symbol for a voltmeter to measure the voltage across lamp L.	            (2)

4. A resistor is added to the above circuit as shown

- What happens to the current flowing in the circuit

- What happens to the brightness of the bulbs    				(2)

5. State two uses of variable resistors						(2)

6. A variable resistor is used in the circuit below to vary the speed of a motor.

Explain what happens to the speed of the motor if the resistance of the variable resistor is increased								(2)

7. Copy and complete the sentence below

An ammeter is connected in __________________ Current is measured in _____

A voltmeter is connected in __________________Voltage is measured in ______

(2)

ELECTRICITY 4

1. Consider the following circuit

- What is the current through the lamp

- What is the voltage across the lamp				(2)

2. Consider the following circuit. The lamps are identical

- Are the lamps in parallel or series

- What is the current through each lamp

- What is the voltage across each lamp				(3)

3. Consider the following circuit in which all the resistors are identical

- What is the current through each resistor

- What is the voltage across each resistor				(2)

4. Consider the following circuit in which a motor is in series with a resistor. The current through the resistor is 0.5A and the voltage across the resistor is 2V

- What is the current through the motor

- What is the voltage across the motor				(2)

5. In the following circuit a lamp is connected in parallel with a resistor across a 12V battery. The current from the battery is 0.8A and the current through the resistor is 0.2A.

- Calculate the current through the lamp

- What is the voltage across the lamp

- What is the voltage across the resistor				(3)

6. Calculate the total resistance in each of the following circuits. Show equation and working.

7. Calculate the total resistance in each of the following circuits. Show equation and working

(4)

ELECTRICITY 5

- The  circuit below is used to determine the resistance of a resistor

(a) What is the component marked x						(1)

(b) A graph is drawn of the voltage against current as shown

Calculate the resistance of the component x					(2)

- x is replaced by a torch bulb and the experiment repeated and a graph drawn as shown

(a) By taking measurements from the graph show what happens to the resistance of the bulb as the current increases							(3)

(b) Explain why this happens							(1)

2. A lamp has a resistance of 960 . It needs to draw a current of 0.25 A to operate at its correct brightness. What size of voltage does it need?		(2)

3. Consider the following circuit

(a) If the resistor is removed from the circuit explain what would happen to the 	brightness of the lamp

(b) The voltmeter reads 10V when the resistor has a resistance of 100Ω. Calculate 	the ammeter reading

(c) Calculate the charge flowing if the current flows for 20seconds		(5)

4.A circuit similar to the above is set up with a different resistor. The voltmeter reading is 10V when the current is 0.05A.

(a) Calculate the resistance of the resistor

(b) If 60 Coulombs of charge flow from the supply, calculate how long the current 	was flowing									(4)

5. Calculate the ammeter reading in the following circuit

(2)

6. Calculate the voltmeter reading in the following circuit

(2)

ELECTRICITY 6

1. The following circuit shows two resistors of 4Ω and 12Ω in parallel

(a) Calculate the equivalent resistance

(b) Calculate the current from the supply

(c) What is the voltage across the 12Ω resistor				           (5)

2. The following circuit shows two resistors of 4Ω and 12Ω in series across a 12V 	supply

- Calculate the equivalent resistance

- Calculate the current from the supply

- What is the current through the 4Ω resistor				(5)

- A 10Ω resistor is connected to a 5V supply as shown and the current switched on for 5minutes

(a) Calculate the current from the supply

(b) Calculate the power from the supply

(c) Calculate the energy given out in 5minutes

(d) Calculate the charge from the supply in 5 minutes				(8)

4.  A heater rated at 12V, 24W is switched on for 10minutes

(a) Calculate the current through the heater

(b) Calculate the energy given out by the heater in this time

(c)Calculate the resistance of the heater				             	(6)

- Power lines have a resistance of 10ohms per metre and carry a current of 20A

Calculate the power lost over a distance of 1km					(3)

- A resistor of resistance 100ohms is connected to a power supply of 10V.

Calculate the power available from the supply					(2)

ELECTRICITY 7

1. Using a ruler copy and complete the following table for output devices

| Output Device | Energy change | Symbol |
| --- | --- | --- |
| Motor |  |  |
| Light emitting diode |  |  |
| Lamp |  |  |
| Loudspeaker |  |  |

(4)													2.Consider the circuit shown below

(a) What is component X

(b) What happens if the component X is reversed in the circuit

(c) What is the purpose of the resistor R

(d) If the operating voltage of the led is 5V calculate the voltage across R

(e) If the current through the resistor is 0.2A calculate the value of R         (6)

3. Consider the diagram shown below

If the voltage across the led is 3V, calculate the voltage across the resistor and hence the resistance of the resistor.							         (3)

4. Consider the diagram shown below

The led has a working voltage of 2V and a power rating of 0.01W. Calculate

- The current through the led

- The voltage across the resistor

- The resistance of the resistor					(5)

5. Consider the following diagram

(a) If the voltage across the resistor is 2V calculate the current through the resistor

(b) Calculate the voltage across the led

(c) Calculate the resistance of the led				           (5)

ELECTRICITY 8

1. Draw the symbol for the following

- Thermistor

- Light dependent resistor							(2)

2. A thermistor has a resistance of 200Ω when placed in a beaker of water at 200C.

- Calculate the current when it is connected across a 5V supply

- The temperature of the water is now changed such that the current is now greater. Explain whether the temperature of the water has been increased or decreased								(4)

3. A light dependent resistor has a resistance of 10k when placed in front of a ray    box. A 5V supply is connected across the ldr.

(a) Calculate the current through the ldr

(b) The intensity of the lamp is changed such that the current has decreased. Explain whether the intensity of the lamp has been increased or decreased

(4)

5. Consider the circuit shown below

- What is component marked X

- Sketch a graph to show how the voltage across X varies with time as the capacitor charges up

(c) Other than the voltage what two changes can be made to the circuit to increase the time taken for X to charge up						           (4)

# Text boxes

1k

2V

v

10k

5mA

4Ω

12Ω

4Ω

12Ω

5V

0.2A

R

5V

R

### 3rd Year Physics

Number :

##### Homework  Sheets

14

13

12

11

10

9

8

1

2

3

4

5

6

7

14

13

12

11

10

9

8

1

2

3

4

5

6

7

A

B

C

D

clock

clock

reset

Electricity and Energy

1

Name:

St. Andrew’s  Academy

Physics Department